## Slide 1: Smith-Chart
Prof. F. Dellsperger
Introduction
to the
Smith Chart

## Slide 2: Smith-Chart
Eq. 1
Eq. 2
Eq. 3
From theory of lines:
Normalized Z = z = r + jx

## Slide 3: Smith-Chart
Representation of Reflection Coefficient in Polar Diagram:

## Slide 4: Smith-Chart
According to Eq.1, each reflection coefficient must also represent a complex impedance Z, or according to Eq.3 a complex normalized impedance z.

## Slide 5: Smith-Chart
Why not overlay a grid with impedance values?
This would help to visualize Eq. 1 and 3.
It would also help to visualize the effect of changing elements in a network.
For example:
For a given load impedance consisting of a serie R – L -network the value of L changes by a certain value.
How does it affect the reflection coefficient (or VSWR)?

## Slide 6: Smith-Chart
Short
Z0
Open
Let‘s first consider a few special points.
Open circuit: R=∞, X=0, (r=∞, x=0)
Z = Z0: R=50, X=0, (r=1, x=0)
Short circuit: R=0, X=0, (r=0, x=0)

## Slide 7: Smith-Chart
Draw the locus for r = 1 (R=Z0) and -∞<x<+∞
x =
-∞
r =
1
-10
-4
-2
-1
-0.5
-0.1
0
+0.1
+0.5
+1
+2
+4
+10
+∞
1
This gives a constant-r-circle for r = 1

## Slide 8: Smith-Chart
Draw the locus for r = 0.5 (R=0.5Z0) and -∞<x<+∞
x =
-∞
r =
0.5
-10
-4
-2
-1
-0.5
-0.1
0
+0.1
+0.5
+1
+2
+4
+10
+∞
1
0.5
This gives a constant-r-circle for r = 0.5

## Slide 9: Smith-Chart
Draw the locus for r = 0.2, 2, 4 and -∞<x<+∞
x =
-∞
r =
0.2
-10
-4
-2
-1
-0.5
-0.1
0
+0.1
+0.5
+1
+2
+4
+10
+∞
1
0.2
0.5
2
-∞
-10
-4
-2
-1
-0.5
-0.1
0
+0.1
+0.5
+1
+2
+4
+10
+∞
-∞
-10
-4
-2
-1
-0.5
-0.1
0
+0.1
+0.5
+1
+2
+4
+10
+∞
4
2
4
More
constant-r-circles

## Slide 10: Smith-Chart
Locus for r = 0.2, 0.5, 1, 2, 4 and -∞<x<+∞
-∞<x<+∞
r =
1
0.2
0.5
2
4
0.2, 0.5, 1, 2, 4
Locus for constant
real part of impedance

## Slide 11: Smith-Chart
Draw the locus for x = 1 (X=Z0) and 0<r<+∞
r =
0
x =
0.2
0.2
0.5
2
0.2
0.5
1
2
4
10
+∞
1
1
2
4
1
This gives a constant-x-circle for x = 1

## Slide 12: Smith-Chart
Draw the locus for x = -1 (X = -Z0) and 0<r<+∞
r =
0
x =
0.2
0.2
0.5
2
0.2
0.5
1
2
4
10
+∞
-1
1
2
4
-1
1
This gives a constant-x-circle for x = -1

## Slide 13: Smith-Chart
Draw the locus for x = 0.2, 0.5, 2, 4, 10 and 0<r<+∞
r =
x =
0.2
0.5
0<r<+∞
+0.2
1
2
4
-1
+0.5
+2
+4
+10
-0.2
-0.5
1
0.2
0.5
2
4
-0.2
-0.5
-2
-4
-2
-4
-10
Locus for constant
imaginary part of impedance

## Slide 14: Smith-Chart
Impedance plane

## Slide 15: Smith-Chart
Impedance plane
Serie L or C
Real part of impedance = constant

## Slide 16: Smith-Chart
Impedance plane
Serie R
Imaginary part of impedance = constant

## Slide 17: Smith-Chart
|| = 0.6
VSWR = 2
Impedance plane
Circles of
constant || and VSWR

## Slide 18: Smith-Chart
Impedance plane
Serie transmission line
with Z = Z0
VSWR = 4
The center of constant VSWR-circle is the center of Smith-Chart if Smith-Chart is normalized to the line impedance.

## Slide 19: Smith-Chart
Admittance chart:
Normalized Y= y
Eq. 4
Eq. 5
Eq. 6

## Slide 20: Smith-Chart
According to Eq.4, each reflection coefficient must also represent a complex admittance Y, or according to Eq.6 a complex normalized admittance y.

## Slide 21: Smith-Chart
Admittance plane
Using the similar procedure as with the impedance plane we get circles for constant conductance g and arcs for constant susceptance b.
Locus for constant
imaginary part of
admittance
Locus for constant
real part of admittance

## Slide 22: Smith-Chart
Admittance plane
Parallel L or C
Real part of admittance = constant

## Slide 23: Smith-Chart
Imittance chart
Overlay of impedance and admittance plane

## Slide 24: Smith-Chart
Constant-Q circles

## Slide 25: Smith-Chart
Example using „Smith“-Software
www.fritz.dellsperger.net

## Slide 26: Smith-Chart
L-networks for maching Z2 to Z0

## Slide 27: Smith-Chart
L-networks for maching Z2 to Z0

## Slide 28: Smith-Chart
Software: Smith V4.0 www.fritz.dellsperger.net